## Slide 1
Faculty Of Engineering
Department Of Electrical And Electronics Engineering
Bachelor Of Engineering In Telecommunication Engineering
Cyber security evaluation and mitigation for future wireless networks,5G, IoT and cloud storage networks
(An Offensive and Defensive Technical Approach)
Final Year Project Proposal, EE421
By: Muhanguzi Tobias, CCNA, IEEE, ISOC. 15/U/7774/ETE/PE
Supervisor: Mr. Kitone Isaac
Kyambogo University

## Slide 2
Kyambogo University
Abstract
In the near future, after, 2020 when 5G has been launched, 5G and the next generation networks will be characterized by; low latency, improved throughout, low transmit-recieve power, and * consequently improved QOS. This has been proposed to be achieved by, mmwave, MU-MIMO, SDR(C-RAN), MEC, NFV, and SDN, with IoT and Cloud computing as major enablers. Due to softwarization ie SDN, and network slicing ie NFV, new cyber security threat vectors, are introduced. On that issue, 5G will be the cellular radio for IoT, and cloud computing networks to ensure total QoS, a proper security architecture should be developed. In this paper, I will cover; (1) The basic cyber security concepts, like; risk management, assurance, secSDLC models, encryption and ACs models, the 5G, IoT and Cloud computing security architectures/frameworks, and cyber policy of Uganda, and the USA. (2) For each of the architectures, I shall demonstrate the countermeasures to the threat vectors cited, demonstrate network security techniques , and encryption algorithms. Part (1) will be theoretical, and Part (2) will be a practical demo of cyber security tools, ie Defensive (Proactive), and Offensive (Reactive).
Key terms: secSDLC, 5G, 3GPP, 5GPPP, mmwave, MEC, NFV, SDN, SDR, IoT, ACs, eMBB, mMTC, uRLLC, PaaS, IaaS, SaaS, smart city, smart grid, smart home, etc
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 3
5G will be the network for the future QoS demands, with the major enablers being; cloud services and IoT. 5G is on trial in most parts of Africa, including Uganda as per the time of carrying out this research(2018). There are four fundamental requirements for a modern communication network, which include, Data rate/throughput capacity, Processing power of network equipment, Functional Redundancy and ether channels, and most importantly cyber-security, all of which contribute to QoS Realization. Security of huge amounts of data (big data) on 5G, IoT, and Cloud computing networks and storage, should be handled with great concern. However, the field of cyber security has grown in the recent years, due to the rise of cyber crimes with well defined CBK, and approaches.
Background
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 4
Background | Big picture
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 5
Background | Big picture…cont’d
Insert some details on 5G
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
eMBB
mMTC
uRLLC
Others
IEEE 802.11ac

## Slide 6
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
IoT is the network of physical objects not limited to devices, vehicles, buildings, and other items embedded with electronics, software, sensors, and network connectivity that enables these objects to collect and exchange data
Background | Big picture…cont’d

## Slide 7
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Background | Big picture…cont’d

## Slide 8
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
With the emergence of the Internet of Things (IoT), there is a lot more data to manage and secure, plus the fact that we have expanded storage capacity and storage services through the cloud and virtualization, this has led to the exponential growth of data. This data has created a new area of interest in technology and business called “Big Data". With the velocity, volume, and variety of data generated by the IoT and the daily operations of business, the confidentiality, integrity and availability of this data is vital to the survival of the organization.1
Background | Big picture…cont’d

## Slide 9
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Background | Big picture…cont’d

## Slide 10
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Definition from NIST (National Institute of Standards and Technology) Cloud computing is a model for enabling convenient, on-demand network access to a shared pool of configurable computing resources (e.g., networks, servers, storage, applications, and services) that can be rapidly provisioned and released with minimal management effort or service provider interaction. This cloud model promotes availability and is composed of five essential characteristics, three service models, and four deployment models.
Background | Big picture…cont’d

## Slide 11
The increasing demands for real-time communication/ streaming 4k videos, gaming , VR, MR and AR and IoT/ IoE (smart home, smart grid, smart city, v2x) that put a constraint on traditional storage, raising need for cloud computing. The data on a network includes personal health data, agriculture, education, e-government, e-commerce including, the increasing electronic money transfers etc. All together with the effort of the government to digitize all communication, all these services , and efforts generate huge amounts of data, Big-data, this poses a problem ensuring security, CIA Triad. I have singled out cyber-security to be the focus of this paper. All said, the security of data put on the network; in transit, and in cloud and other storage servers has to be handled with great concern. With the proposed 5G network to be rolled-out by 2020, I advocate for a secure architecture, by reviewing the security layers.
Problem statement
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 12
Objectives
General Objectives;
Cyber security evaluation and mitigation for future wireless networks, 5G, IoT and cloud storage networks (an Offensive and Defensive Technical Approach)
Specific Objectives;
To carry out research on cyber security risk management, models, frameworks, and roadmap.
To carry out research on encryption algorithms of wireless networks, and Access control models
To carry out research on 5G, IoT and Cloud network architecture.
To develop two MATLAB Applications; one that hinds the characters of a password on login and implements minimum login requirements , and another that generates munged passwords to ensure password hardening.
To carry out research on cyber security policies.
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 13
5G has two major enablers which are NFV, and SDN, and is the idle network for IoT and cloud storage networks. The network virtualization and softwarization introduces new attack vectors, that will require different Countermeasures, like Authentication, Access control models, etc. Therefore it is worth it, to review the proposed 5G security architecture. Considering the fact that Uganda is preparing for 5G roll out, currently in trial versions, Start-ups are implementing cloud systems, and IoT systems, like automation of different activities in health, agriculture, power grid, government( CCTV public surveilance cameras) and mobile banking/mobile money and education(e-learning platforms ) all of which require internet connectivity (cellular 5G connectivity) , security of data transfers should be secured, hackers can cost a company a great deal of money, reputation, and test its competence to protecting the information of its customers.
Justification
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 14
Significance of the study
This study will Create a practical understanding of cyber security, policies and practices that accrue to Computer security, Security Systems Software Development Life Cycle (secSDLC), Network security for the future wireless networks that carry customer critical data used and generated by IoE, IoT, and in the Cloud.
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 15
The following practical activities will be carried out during the course of the project:
Wireless Encryption algorithms, munged passwords with MATLAB
History of hacking and Ethical hacking.
Tools used in penetration testing, social engineering and vulnerability tests with kali linux for wireless networks.
Cyber Security management models with GNS3 simulation (secSDLC)
Security with python programming.
Security in the application layer and network layer (ipv4 and ipv6) analysis with wireshark, Snort (Network security systems, IDS/IPS, honey pots, DNZ, TLS, NTPSec, IPSec, DNSSec).
5G, IoT (NFC, Smart grid) cyber security and cloud storage security concerns and countermeasures
Cyber security policies, including the GDPR. And UGCERT activity review
Scope of the project
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 16
Methodology
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 17
cyber security concept research
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Cyber security mind map
The orange book
X.800 CBK-Common Body of Knowledge-CISSP, Encryption, ACs models Software Dev't Life Cycle security Software assurance, Risk management, Competency, Models, Roadmaps, and Frameworks Infosec and DevOps, Vulnerability assessment, patch management, and artifact handling.
Cyber Theats

## Slide 18
Network cyber security
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Understanding the physical network/ topology Device configuration for security, and disabling inactive protocols Security attack window for 5G, IoT and Cloud computing. Hardware and software security tools; honey pots, DMZ, Fire Walls, IDS +IPS, VPNs, and VLANs, IPsec...

## Slide 19
5G
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
5G architecture according to 5GPPP 5G players; ITU, 3GPP, 5GPPP, China mobile, AT&T, Korea Major enablers
SDN-slicing & it's need
NFV-virtualization & it's need
IoT, RFID, NFC and bigdata dilemma
5G security architecture Construction model according to 5GPPP New attack vectors due to NFV, and SDN + threats Counter measures Encryption techniques for 5G

## Slide 20
IoT
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
IoT architecture Enablers Construction model IoT security architecture Construction model Threats and attack window Counter measures and policy regulation Incidences

## Slide 21
Cloud computing
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Cloud computing architecture Enablers Construction model approaches:: service--PaaS, SaaS, XaaS, deployment--public, private, hybrid Cloud computing security architecture Construction model Threats and attack window Counter measures and policy regulations Incidences of attacks

## Slide 22
Counter measures
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 23
Cyber security counter measures
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Security Audits or Assessments, according to guidelines :: character substitution password login application Infosec :: encryption algorithms for wireless networks :: pin hardening tranlation application. online protection :: malware script for phishing Configuration and Maintenance of Security Development of Security Tools :: munged password application in python Intrusion Detection Services using snort, wireshark Security-Related Information Dissemination.
Proactive/ Defensive tools

## Slide 24
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
Kali Linux operating system tools/ "backtrack" Social Engineering Alerts and Warnings:: pen-testing models Incident Handling, Incident analysis, Incident response support, Incident response coordination, Incident response on site Vulnerability Handling, Vulnerability analysis, Vulnerability response, Vulnerability response coordination Recovery handling
Reactive/ Offensive tools

## Slide 25
Attack history statistics and their impact
Ug-Cert operations
GDPR
Other policies, relating to cyber security in Uganda, and a model country
Law and policy for Cyber security
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 26
The following will be incurred as the project goes on to completion
Estimated budget for the project
Kyambogo University
Item | Amount (Uganda Shillings)
LAPTOP | 1,400,000
TEXT BOOKS | 220,000
SOFTWARE | 300,000
Total | 1,920,000
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 27
Proposed project schedule
2018/2019 | 2018 |  |  |  |  | 2019 |  |  |  | 
 | Aug | Sept | Oct | Nov | Dec | Jan | Feb | March | April | May
Research |  |  |  |  |  |  |  |  |  | 
Matlab programming |  |  |  |  |  |  |  |  |  | 
Proposal writing |  |  |  |  |  |  |  |  |  | 
Presentation of Topic |  |  |  |  |  |  |  |  |  | 
Introduction to Cyber security |  |  |  |  |  |  |  |  |  | 
Python programming |  |  |  |  |  |  |  |  |  | 
Kali Linux |  |  |  |  |  |  |  |  |  | 
Policy research |  |  |  |  |  |  |  |  |  | 
Presentation |  |  |  |  |  |  |  |  |  | 
Report Writing |  |  |  |  |  |  |  |  |  | 
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika

## Slide 28
References
https://www.offensive-security.com/kali-linux-arm-images/
https://github.com/offensive-security/kali-arm-build-scripts
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika
https://www.edrawsoft.com/
Big Data For Dummies by Judith Hurwitz, Alan Nugent, Dr. Fern Halper,
and Marcia Kaufman, Published by John Wiley & Sons, Inc.111 River Street Hoboken, NJ 07030-5774
www.wiley.com Copyright © 2013 by John Wiley & Sons, Inc., Hoboken, New Jersey
https://373583482.netacad.com/courses/696516
https://5g-ppp.eu/white-papers/
Michael Roland Security Issues in Mobile NFC Devices ISSN 2192-2810 ISSN 2192-2829 (electronic)
T-Labs Series in Telecommunication Services ISBN 978-3-319-15487-9 ISBN 978-3-319-15488-6 (eBook)
DOI 10.1007/978-3-319-15488-6
Cloud Computing Security - Foundations and Challenges (2016) (Pdf) Gooner

## Slide 29
Thank you
Kyambogo University
© Muhanguzi Tobias, 15/U/7774/ETE/PE, https://github.com/marydovika